## Slide 1: MARQUIS TECHNOLOGIES
Drive Routes - Chile/Santiago

## Slide 2
Santiago (Chile)
Country | Chile
Continent | America
City | Santiago
Time Zone | GMT -4 Hour
International Dialing Code | +56
VISA | NO NEED
VISA Duration | 90 days
VISA Fees | TBC
VISA Requirements | 
Yellow Fever Vaccination Certificate | Not Required

## Slide 3
Operators in Chile
MCC | MNC | Operator | Bands (MHz)
730 | 1 | ENTEL | GSM 900/1900, WCDMA 900/1900, LTE 700/2600/1900
730 | 2 | MOVISTAR | GSM 850/1900, WCDMA 850/1900, LTE 700/2600
730 | 3 | CLARO | GSM 850/1900, WCDMA 850/1900, LTE 700/2600/1900
730 | 9 | WOM | GSM 850/1900, WCDMA 850/1900/1700/2100, LTE 700/2600/1700/2100

## Slide 4: Operators and Related Information
All the operators are having FDD LTE implementation
ENTEL- Supports VoLTE, VoWifi, LTE, CA, WCDMA and 2G
MOVISTAR- Supports VoLTE, VoWifi, LTE, CA,WCDMA and 2G
CLARO- Supports VoLTE, VoWifi, LTE, CA, WCDMA and 2G
WOM- Supports VoLTE, ViLTE, VoWifi, LTE, WCDMA and 2G
MMS not supported by all operators.

## Slide 5: General Info of Operators
Movistar and Entel remain the market leaders, with a similar market share, while Claro accounts for about a quarter of the market
WOM extends roaming agreement with Entel for LTE services.
Movistar and Entel extend LTE-A capabilities.

## Slide 6: USSD codes for balance check
All Carrier balance check: *103#

## Slide 7: Supplementary Services
ALL carrier support Call forwarding, Call Waiting
Claro doesn’t support call barring.

## Slide 8: MCC MNC for Santiago/Chile Operators:-
MCC MNC for Entel 2G/3G/4G: 730 01
MCC MNC for Movistar 2G/3G/4G: 730 02
MCC MNC for Claro 2G/3G/4G: 730 03
MCC MNC for WOM 2G/3G/4G: 730 09

## Slide 9
RSRP Criteria
Near Cell :-Stationary: RSRP : -55dbm to -85dbm
Cell Edge :-Stationary: RSRP : -95dbm to -110dbm
Mixed :-Mobility: RSRP : -55dbm to -120dbm

## Slide 10
Drive Routes
SRVCC (4G > 3G ) for Entel operator – Parking lot (Don Carlos restaurant) in underground -1 close to the bathroom, need to walk from the stairs.

## Slide 11: Out of Service location for all operators: Basement of Hotel Plaza el Bosque Ebro: Lat: -33.415016, Long: -70.602103

## Slide 12: Cell edge location for Entel LTE Band B2 at Lausana Plaza Lat: -33.327105, Long: -70.504799

## Slide 13: Entel LTE Near Cell for B7, B28 Lat: -33.354434, Long: -70.526526

## Slide 14: LTE Cell edge location for WOM, Movistar, Claro operator Lat: -33.326054, Long: -70.504027

## Slide 15: LTE Near cell location for Entel, WOM, Claro and Movistar operator Lat: -33.377060, Long: -70.536726

## Slide 16: Entel IRAT reselection location LTE > UTRAN

## Slide 17: WOM SRVCC to UTRAN cell location Lat: -33.352769, -70.518512

## Slide 18: Claro, Movistar SRVCC to UTRAN location at Lausana Plaza –B2 Lat; -33.327512, Long: -70.504938

## Slide 19: Drive route Mixed coverage Casa Matriz > Falabella

## Slide 20: Drive Route Mixed coverage El Rodeo > Lausana Plaza

## Slide 21
Thank You