## Slide 1: MARQUIS TECHNOLOGIES
Drive Route – Hyderabad(India)
MD Javeed

## Slide 2
Hyderabad
Country | India
Continent | Asia
State | Telangana
City | Hyderabad
Time Zone | GMT + 5:30
International Dialing Code | +91

## Slide 3
Operator Information
MCC | MNC | Operator | Bands (MHz) & E-ARFCN
405 | 854 | Reliance JIO | LTE 2300 MHz (TDD) Band 40. E-ARFCN- 39225
 |  |  | LTE 850 MHz (FDD) Band 5 E-ARFCN-2540
 |  |  | LTE 1800 MHz (FDD) Band 3
 |  |  | E-ARFCN-1454

## Slide 4
Additional Information
MMS is not supported by RJIO.
L to W and W to L Redirection and reselection is not supported in Hyderabad.
Inter frequency reselection and redirection is supported.
We could not observe Volte Call Handover from Band 3 to Band 40.

## Slide 5
Drive Route
Band 40 (TDD) Near Cell | Band40 (TDD) <-> Band 3 (FDD) Reselection
Band 40 (TDD) Edge Cell | Band40 (TDD) <-> Band 3 (FDD) Reselection
Band 3 (FDD) Near Cell | Mixed Mobility Route-1
Band 3 (FDD) Edge Cell | Mixed Mobility Route-2

## Slide 6
BAND40 Near Cell
Location:-Victory Restaurant, Chanda nagar, Old-Mumbai highway
Lat :-17.494973
Long :-78.325487

## Slide 7
BAND40 Edge Cell
Location:-Hill Country Properties, Nizampet
Lat :-17.530295
Long :-78.375560

## Slide 8
BAND5 Near Cell
Location:-
Bahar Cafe,6th Phase, KPHB
Lat :-17.485714
Long :-78.390533

## Slide 9
BAND5 Edge Cell
Location:- Hyderabad University, HCU road
Lat :-17.463005
Long :-78.334980

## Slide 10: Band 3 Near Cell

## Slide 11: Band 3 Edge Cell

## Slide 12: Band40<->Band3 Reselection
Location:- Quality Inn
Starting Point :-
Lat :-17.429375
Long :-78.374859
Ending Point :-
Lat :- 17.432109
Long :-78.374804

## Slide 13: Band40<->Band3 Reselection
Location:- JDA software Pvt. Ltd., Deloitte
Starting Point :-
Lat :-17.441803
Long :-78.373140
Ending Point :-
Lat :- 17.444249
Long :- 78.367035

## Slide 14
Mixed Mobility Route1
(Hitech City  JNTU Nizampet  Bacchupally  Miyapur  Madinguda HCU  Gachibowli  Hitech)
Starting Point :-
Lat :-17.441858
Long :-78.380164
Ending Point :-
Lat :- 17.439048
Long :- 78.376927
RSRP Level | 
 | -60 to -70
 | -70 to -80
 | -80 to -90
 | -90 to -100
 | Above -100

## Slide 15
Mixed Mobility Route2
(Hitech City  Jubilee Hills Banjara Hills Necklace Road  Begumpet  Mehdipatnam  Raidurgam  Hitech)
Starting Point :-
Lat :-17.441858
Long :-78.380164
Ending Point :-
Lat :- 17.439048
Long :- 78.376927
RSRP Level | 
 | -60 to -70
 | -70 to -80
 | -80 to -90
 | -90 to -100
 | Above -100

## Slide 16
Drive Route_HYD
Operator: Airtel 4G LTE
Mode: Idle & Connected

## Slide 17: Introduction:
LTE BASIC SPECIFICATIONS | 
PARAMETER | DETAILS
Peak downlink speed (Mbps) | 31Mbps
Peak uplink speeds (Mbps) | 19Mbps
CSFB | Supported, 4G to 3G/2G
Channel bandwidths (MHz) | 5-DL Bandwidth 5-UL Bandwidth
Duplex schemes | FDD
Infra Vendor | Ericsson
Latency | Idle to active less than 100ms Small packets ~10 ms
Spectral efficiency | Downlink: 3 - 4 times Rel 6 HSDPA Uplink: 2 -3 x Rel 6 HSUPA
Access schemes | OFDMA (Downlink) SC-FDMA (Uplink)
DRX | 1280

## Slide 18: NEAR CELL & EDGE CELL SPOTS OF HYDERABAD

## Slide 19: Route: Hi-Tech City, Madhapur, Durgamcheruvu Mode: Idle

## Slide 20: Route: Hi-tech City, Raidurgam, Jubilee Hills Mode: Idle

## Slide 21: Route: Hi-tech City, Rethibowli, Masab tank, Lakdikapul Mode: Idle

## Slide 22: Route: Hi-tech City, Domalguda, West Marredpally, Musheerabad Gandhi Hospital Mode: Idle

## Slide 23: Route: Hi-tech City, Lakdikapul, Nampally, Abids, Koti Mode: Idle

## Slide 24: Route: Hi-Tech City, Jubilee Hills Road No-45, Banjar hills, KBR Park Mode: Idle

## Slide 25: Route: Hi-tech City, Masab tank, Banjara hills Road No-1 Mode: Idle

## Slide 26: Route: Shaikpet Dargah, Rethibowli, Mehdipatnam Mode: Idle

## Slide 27: Route: Hi-tech City, Jubilee Hills, Banjara hills Road No-12, Apollo Hospital Jubilee Hills Mode: Idle

## Slide 28: Route: Hi-Tech City, Shaikpet, Tolichowki, Raidurgam Mode: Idle

## Slide 29: Route: BHEL, Madinaguda, Hafeezpet, Bachupally Mode: Idle

## Slide 30: Route: Hi-tech City, Jeedimetla, IMAX Road Mode: Idle

## Slide 31: Route: Hi-tech City, Moghalpura, Alijah Kotla, Talab Katta Mode: Idle

## Slide 32: Route: Hi-tech City, Kondapur, Hi-tex Mode: Idle

## Slide 33: Route: Hi-tech City, Rajendernagar, Attapur, Hasan Nagar, Langer House Mode: Idle

## Slide 34: Route: Hi-tech City, Shaikpet Dargah, Tolichowki Mode: Idle

## Slide 35: IRAT From 4G To 3G & 3G To 2G

## Slide 36: IRAT Route: Hi-tech City To Movie Towers Mode: Idle

## Slide 37: Out Of Service (OOS) Mode: LTE ONLY

## Slide 38: OOS Route: Hi-Tech City To Shankarpally Road Mode: LTE Only

## Slide 39: Redirection From 4G To 3G Mode: Connected

## Slide 40: Route: Hi-Tech City To ISB Road, Financial District IRAT Redirection

## Slide 41: Route: Hi-Tech City To Gandipet

## Slide 42: Route: Hi-Tech City To Bachupally Road

## Slide 43: Route: Hi-Tech City To Coca-Cola Factory, Bachupally Road

## Slide 44: Route: Hi-Tech City To Rajiv Gandhi Nagar, Nizampet

## Slide 45: Route: Hi-Tech City To Quthbullapur

## Slide 46: IRAT Reselection From 4G To 3G Mode: Idle Note:- While performing Reselection I have seen Reselection Failures at many places, because 4G is directly switching to GSM not to 3G, at only one place, I have seen Idle Reselection is happening successfully (2/10). So, at present Reselection is Blocked, till the issue gets resolved.

## Slide 47: Route: Hi-Tech City To Movie Towers

## Slide 48: Operator Information
Operator | MCC-MNC | Bands (MHz) | DRX value
Idea | 404-07 | 4G:- LTE (5 MHz) ARFCN: 1418 | 4G:-1280

## Slide 49: Operator Information
Functionality | Idea
Website: http://www.ideacellular.com/ WAP APN: ideainternet | 
Customer care | 121
MNC | 07
Bands supported | EDGE/GPRS/GSM 900 MHz
 | HSDPA / UMTS 2100
 | LTE 1800 MHz –FDD(Band 3)
USSD | To check MDN:*1#
 | Balance check: *121#
 | Data Balance check: *125#
VoLTE | Not Supported
CSFB | Supported
MMS support | Not Supported

## Slide 50: Drive Route
Near Cell :-Stationary: RSRP: -65dbm to -75dbm
Cell Edge :-Stationary: RSRP : -100dbm to -105dbm
Mixed :-Mobility: RSRP : -65dbm to -120dbm

## Slide 51: Near Cell: HDFC Bank, Hitech City
RSRP: -65dbm to -75dbm
LAT: 17.44363 LONG: 78.379956

## Slide 52: Near Cell: Sarojini Eye Hospital, Mahdipatnam
RSRP: -65dbm to -75dbm
LAT: 17.391636 LONG: 78.440065

## Slide 53: Near Cell: NMDC, Masab Tank
RSRP: -65dbm to -75dbm
LAT: 17.391636 LONG: 78.440065

## Slide 54: Near Cell: JayaBhusan Hospital, Mahdipatnam
RSRP: -65dbm to -75dbm
LAT: 17.393948 LONG: 78.438958

## Slide 55: Edge Cell: LB Stadium Road, Band Colony, Adarsh Nagar
RSRP: -95dbm to -105dbm
LAT: 17.401107 LONG: 78.472396

## Slide 56: Edge Cell: Passport Office, Towlichowki
RSRP: -95dbm to -105dbm
LAT: 17.401107 LONG: 78.472396

## Slide 57: Edge Cell: Raidurgam Police Station
RSRP: -95dbm to -105dbm
LAT: 17.423079 LONG: 78.377112

## Slide 58: Edge Cell: Nissan Motors Showroom
RSRP: -95dbm to -105dbm
LAT: 17.437468 LONG: 78.374268

## Slide 59: L2W Reselection/ Redirection: MindSpace Circle, Bio-Diversity

## Slide 60: L2W Reselection/ Redirection: Himayat Sagar Road

## Slide 61: L2W Reselection/ Redirection: Microsoft Gate No.1, Gachibowli

## Slide 62
Mixed Mobility: Cyber Tower to Financial Disrtict
Starting Point :-
Lat :- 17.450368
Long :- 78.381052
Ending Point :-
Lat :- 17.410798
Long :- 78.341552
RSRP Level | 
 | -70 to -80
 | -80 to -90
 | -90 to -100
 | Above -100
RSRP Level | 
 | -70 to -80
 | -80 to -90
 | -90 to -100
 | Above -100

## Slide 63
Mixed Mobility: Platina Gachibowli to Assembly Nampally
Starting Point :-
Lat :- 17.449059
Long :- 78.363290
Ending Point :-
Lat :- 17.401836
Long :- 78.469226
RSRP Level | 
 | -70 to -80
 | -80 to -90
 | -90 to -100
 | Above -100
RSRP Level | 
 | -70 to -80
 | -80 to -90
 | -90 to -100
 | Above -100

## Slide 64: THANK YOU
MARQUIS TECHNOLOGIES
www.marquistech.com