## Slide 1: MARQUIS TECHNOLOGIES
Drive Route –Airtel, VI & Reliance JIO (FDD/TDD) LTE
Location : Jamnagar

## Slide 2: Operator Information:
Operator | JIO 4G
MCC | 405
MNC | 857
APN | jionet
Operator | Airtel 4G
MCC | 404
MNC | 98
APN | airtelgprs.com
Operator | VI
MCC | 404
MNC | 05
APN | internet
Operator | BSNL
MCC | 404
MNC | 57
APN | Bsnlnet

## Slide 3: Operator Information 1
Functionality | Airtel
Website: https://www.airtel.in/ WAP APN: airtelgprs.com | 
Customer care | 121
MNC | 98
Bands supported | Both FDD and TDD
 | LTE 2300 MHz – TDD(Band 40)
 | LTE 1800 – FDD(Band 3) LTE 2100 – FDD (Band 1)
USSD | To check MDN: *282#
 | Balance check: *123#
 | To check all services: *121#
VoLTE | Supported
VoWiFi | Supported
CSFB | Supported (CSFB to 2G)

## Slide 4: Operator Information 2
Functionality | RELIANCE JIO
Website: https://www.jio.com WAP APN: jionet | 
Customer care | 198
MNC | 857
Bands supported | Both FDD and TDD
 | LTE 2300 MHz –TDD(Band 40)
 | LTE 850 MHz – FDD(Band 5)
 | LTE 1800 MHz –FDD(Band 3)
USSD | NA
 | NA
 | NA
VoLTE | Supported
VoWiFi | Supported
CSFB | Not Supported

## Slide 5: Operator Information 3
Functionality | VI
Website: https://www.myvi.in WAP APN: internet | 
Customer care | 198
MNC | 05
Bands supported | Both FDD and TDD
 | LTE 2300 MHz –TDD(Band 40)
 | LTE 2500 MHz –TDD(Band 41)
 | LTE 1800 MHz –FDD(Band 3) LTE 900 MHz –FDD(Band 8) LTE 2100MHZ-FDD(Band 1)
USSD | To check MSISDN :*199#
 | Recharge : *199*5#
 | Balance check : *199*2#
VoLTE | Supported
VoWiFi | Not Supported
CSFB | Supported (CSFB to 2G/3G)

## Slide 6: Drive Route
Near Cell : Stationary: RSRP : -65dbm to -75dbm
Edge Cell : Stationary: RSRP : -95dbm to -110dbm
Mixed : Mobility: RSRP : -65dbm to -110dbm

## Slide 7: Near Cell (Airtel)
Near cell | longitude | latitude | RSRP (dbm) | Cell id | E-ARFCN
1 | 70.058708 | 22.493786 | -73 | 4 | 1559
RSRP Range for Near Cell :
-65dbm to -75dbm
Street no-4 macharsheri ,jamnagar

## Slide 8: Edge Cell (Airtel)
Edge cell | longitude | latitude | RSRP (dbm) | Cell id | E-ARFCN
1 | 70.056468 | 22.493691 | -106 | 8 | 39348
RSRP Range for Edge Cell :
-95dbm to -110dbm
Hanuman mandir,
near Gandhinagar railway
st jamnagar

## Slide 9
Mixed Coverage Area for Airtel

## Slide 10
Airtel Inter Band HO
Band 1 BAND 3 BAND 40

## Slide 11: MATT Tool InterBand Handover Results for Airtel

## Slide 12: Near Cell (Reliance JIO)
Near cell | longitude | latitude | RSRP (dbm) | Cell id | E-ARFCN
1 | 70.057446 | 22.492513 | -72 | 18 | 38750
RSRP Range for Near Cell :
-65dbm to -75dbm
Lord shiv temple,Gandhi
Nagar,Jamnagar

## Slide 13
Edge Cell (Reliance JIO)
Edge Cell | longitude | latitude | RSRP (dbm) | Cell id | E-ARFCN
1 | 70.056583 | 22.495420 | -96 | 16 | 38750
RSRP Range for Edge Cell :
-95dbm to -110dbm
Saibaba mandir,
jamnagar

## Slide 14
Mixed Coverage Area for Reliance JIO

## Slide 15: Inter Band Handover (FDD-TDD) for JIO 4G
Band 40 Band 5 Band 3

## Slide 16: MATT Tool InterBand Handover Results for Jio

## Slide 17: Near Cell for VI:
Near Cell | longitude | latitude | RSRP (dbm) | Cell id | E-ARFCN
1 | 70.058835 | 22.493796 | -70 | 42 | 1309
Lord shivtemple
street no-4
jamnagar
RSRP Range for Near Cell :
-65dbm to -75dbm

## Slide 18: Edge Cell for VI:
Edge cell(EC) | longitude | latitude | RSRP (dbm) | Cell id | E-ARFCN
1 | 70.051735 | 22.489040 | -101 | 81 | 40090
RSRP Range for Edge Cell :
-95dbm to -110dbm
Bedi overbridge,
near Jamnagar
railway
station

## Slide 19: Mixed Coverage Area for VI:

## Slide 20: VI Band Handover
Band 8 Band 3 Band 41

## Slide 21: MATT Tool InterBand Handover Results for VI

## Slide 22: G-net Tracker Drive Route

## Slide 23: Drive Route

## Slide 24: THANK YOU
MARQUIS TECHNOLOGIES