## Slide 1: MARQUIS TECHNOLOGIES
Drive Route –Airtel, VI & Reliance JIO (FDD/TDD) LTE
Location : Nagpur

## Slide 2: Operator Information:
Operator | JIO 4G
MCC | 405
MNC | 864
APN | jionet
Operator | Airtel 4G
MCC | 404
MNC | 90
APN | airtelgprs.com
Operator | VI
MCC | 404
MNC | 22
APN | internet
Operator | BSNL
MCC | 404
MNC | 66
APN | Bsnlnet

## Slide 3: Operator Information 1
Functionality | Airtel
Website: https://www.airtel.in/ WAP APN: airtelgprs.com | 
Customer care | 121
MNC | 90
Bands supported | Both FDD and TDD
 | LTE 2300 MHz – TDD(Band 40)
 | LTE 1800 – FDD(Band 3) LTE 2100 – FDD (Band 1)
USSD | To check MDN: *282#
 | Balance check: *123#
 | To check all services: *121#
VoLTE | Supported
VoWiFi | Supported
CSFB | Supported (CSFB to 2G)

## Slide 4: Operator Information 2
Functionality | RELIANCE JIO
Website: https://www.jio.com WAP APN: jionet | 
Customer care | 198
MNC | 864
Bands supported | Both FDD and TDD
 | LTE 2300 MHz –TDD(Band 40)
 | LTE 850 MHz – FDD(Band 5)
 | LTE 1800 MHz –FDD(Band 3)
USSD | NA
 | NA
 | NA
VoLTE | Supported
VoWiFi | Supported
CSFB | Not Supported

## Slide 5: Operator Information 3
Functionality | VI
Website: https://www.myvi.in WAP APN: internet | 
Customer care | 198
MNC | 22
Bands supported | Both FDD and TDD
 | LTE 2300 MHz –TDD(Band 40)
 | LTE 2500 MHz –TDD(Band 41)
 | LTE 1800 MHz –FDD(Band 3) LTE 900 MHZ-FDD(Band 8) LTE 2100 MHz-FDD(Band 1)
USSD | To check MSISDN :*199#
 | Recharge : *199*5#
 | Balance check : *199*2#
VoLTE | Supported
VoWiFi | Not Supported
CSFB | Supported (CSFB to 2G)

## Slide 6: Drive Route
Near Cell : Stationary: RSRP : -65dbm to -75dbm
Edge Cell : Stationary: RSRP : -95dbm to -110dbm
Mixed : Mobility: RSRP : -65dbm to -110dbm

## Slide 7: Near Cell (Airtel)
Near cell | longitude | latitude | RSRP (dbm) | Cell id | E-ARFCN
1 | 79.078162 | 21.086920 | -63 | 3 | 1500
RSRP Range for Near Cell :
-65dbm to -75dbm
near Jayanti mansion,
Somalwada
Nagpur

## Slide 8: Edge Cell (Airtel)
Edge cell | longitude | latitude | RSRP (dbm) | Cell id | E-ARFCN
1 | 79.079795 | 21.092708 | -99 | 1 | 39150
RSRP Range for Edge Cell :
-95dbm to -110dbm
Manish Nagar,
Nagpur

## Slide 9
Mixed Coverage Area for Airtel

## Slide 10
Airtel Inter Band HO
Band 1 BAND 40 BAND 3

## Slide 11: MATT Tool InterBand Handover Results for Airtel
L1_L40 :2
L1_L3 : 0
L40_L1: 2
L40_L3 3
L3_ L1: 0
L3_L40: 2

## Slide 12
CA Airtel :

## Slide 13: Near Cell (Reliance JIO)
Near cell | longitude | latitude | RSRP (dbm) | Cell id | E-ARFCN
1 | 79.077795 | 21.087061 | -76 | 24 | 38750
RSRP Range for Near Cell : -65dbm to -75dbm
Somalwada,
Nagpur

## Slide 14
Edge Cell (Reliance JIO)
Edge Cell | longitude | latitude | RSRP (dbm) | Cell id | E-ARFCN
1 | 79.079739 | 21.092523 | -94 | 22 | 38750
RSRP Range for Edge Cell :
-95dbm to -110dbm
Somalwada,
Nagpur

## Slide 15
Mixed Coverage Area for Reliance JIO

## Slide 16: Inter Band Handover (FDD-TDD) for JIO 4G
Band 40 Band 5 Band 3

## Slide 17: MATT Tool InterBand Handover Results for Jio
L40_L5 : 1
L5_L3 : 0
L5_L40: 1
L3_L5 : 0
L40_ L3: 1
L3_L40: 0

## Slide 18
CA Jio :

## Slide 19: Near Cell for VI:
Near Cell | longitude | latitude | RSRP (dbm) | Cell id | E-ARFCN
1 | 79.078948 | 21.091033 | -64 | 82 | 3601
near KRIMS hospital,
Manish Nagar,
Nagpur
RSRP Range for Near Cell :
-65dbm to -75dbm

## Slide 20: Edge Cell for VI:
Edge cell(EC) | longitude | latitude | RSRP (dbm) | Cell id | E-ARFCN
1 | 79.076124 | 21.7090337 | -109 | 82 | 3601
Somalwada,
Nagpur
RSRP Range for Edge Cell :
-95dbm to -110dbm

## Slide 21: Mixed Coverage Area for VI:

## Slide 22: VI Band Handover
Band 3 Band 8 Band 1 Band 41

## Slide 23: MATT Tool InterBand Handover Results for VI
L40_L41 : 0
L8_L1 : 1
L1_L41: 1
L3_L1 : 1
L41_ L3: 1
L3_L40: 0

## Slide 24
CA VI:

## Slide 25: G-net Tracker Drive Route

## Slide 26: Drive Route

## Slide 27: THANK YOU
MARQUIS TECHNOLOGIES